## Slide 1: 2-bit Branch Predictor
EE-475L Computer Architecture
(Complex Engineering Problem)
Group VI

## Slide 2: Branch Predictor Diagram

## Slide 4: BHT Diagram

## Slide 5: BHT Diagram

## Slide 6: BTB Diagram

## Slide 7: BTB Diagram

## Slide 8: Controller Diagram

## Slide 9: Controller Diagram

## Slide 10: Controller Diagram

## Slide 11: Expected Goals
Stage 1:
  Design a 2-bit branch predictor (BHT, BTB, Controller)
Stage 2:
  Implement the branch predictor designed
Stage 3:
  Test seamless coordination between BHT, BTB and Controller along with their functionality independently and combined.

## Slide 12: Achieved Goals
Stage 1:
  2-bit forward prediction architecture designed.
Stage 2:
  Fully functional BHT, BTB and controller architecture implemented.
Stage 3:
  Simulated the architecture with multiple branch patterns.

## Slide 13: Algorithm
Prediction (Fetch stage):
  If branch inst, use PC to access BHT and BTB.
  BHT gives a 2-bit prediction (NT, WNT, WT, T).
  If taken, BTB provides the target address. Else, BTB provides pc+4.
Decode/Execute Phase:
  Actual result is known now so compare actual outcome with predicted one.
  Update BHT: Adjust internal counter (Increment if branch is taken and decrement if not taken)
  Update BTB: On actual taken branch, save target address ensuring fast access for next prediction

## Slide 14: Results
Simulation of branch instruction,
0x00018a63
Whose target address = 0x0000014
With the pattern
A non-branch instruction at the end to validate our architecture works only for branch instructions.
Actual | Taken | Taken
Predicted | Weakly Not Taken | Taken
 | X | ✓